## Slide 1: Tablets

## Slide 2: Tablets
Definition:
“Solid shaped unit pharmaceutical dosage forms containing drug substances with or without suitable diluents and prepared either by compression or by molding methods”.
Types:
Sublingual tablet, Buccal tablet, Chewable tablet
Compressed tablet, Sugar coated tablet, Filmcoated tablet
Enteric coated tablet, Sustained release tablet

## Slide 3
S.No | Advantages to the Patient | Advantages to the prescriber
1 | Accuracy of dosage | Immediate drug release by sublingual administration
2 | Ease of administration | Patient compatibility
3 | Compactness & portability | Sustained release tablets reduces frequency of dosing
4 | Taste masking of bitter substances by coating | Confidant on adherence to prescription

## Slide 4: Compressed Tablets (CT)
Are formed by compression and contain no special coating.
They are made from powdered, crystalline or granular materials, alone or in combination with binders, disintegrants, controlled-release polymers, lubricants, diluents and, in many cases, colorants

## Slide 5
S.No | Sugar coating | Film coating
1 | Compressed tablets containing a sugar coating | Compressed tablets which are covered with a thin layer or film of a water-soluble polymer material
2 | Different layers of coating are done (Sealant coating, sub coating, sugar coating) | Single layer coating (Polymeric substance with film-forming properties are used, reduces time period required for the coating operation.)
3 | Protects materials sensitive to oxidation, moisture and odor. | Beneficial in covering up drug substances possessing objectionable tastes or odors,
4 | Colored coating | Usually transparent

## Slide 6: Enteric coated tablets
It can be used for tablets containing drug substances which are inactivated or destroyed in the stomach, for those which irritate the mucosa.
These are compressed tablets coated with substances that resist solution in gastric fluid but disintegrate in the intestine.
Can be formulated to delay the release of the Drug .

## Slide 7: Types
Multiple Compressed Tablets (MCT) -These are compressed tablets made by more than one compression cycle.
Multilayered tablets- Such tablets are prepared by compressing additional tablet granulation on a previously compressed granulation. The operation may be repeated to produce multilayered tablets of two or three layers. Special tablet presses are required to make layered tablets

## Slide 8: Press coated tablets
Dry-coated, are prepared by feeding previously compressed tablets into a special tableting machine and compressing another granulation layer around the preformed tablets . They have all the advantages of compressed tablets, i.e, monogramming, speed of disintegration, etc, while retaining the attributes of sugar-coated tablets in masking the taste of the drug substance in the core tablets...
Press-coated tablets also can be used to separate incompatible drug substances In addition, they can provide a means to give an enteric coating to the core tablets. Both types of multiple-compressed tablets have been used widely in the design of prolonged-action dosage forms.

## Slide 9: Modified release tablets
Compressed tablets can be formulated to release the drug slowly over a prolonged period of time. Hence, referred to as Prolonged-Release or Sustained-Release dosage forms as well. These tablets (capsule versions) categorized into three types:
(1) those which respond to some physiological condition to release the drug, such as enteric coatings;
(2) those that release the drug in a relatively steady, controlled manner and
(3) those that combine combinations of mechanisms to release “pulses” of drug, such as repeat-action tablets

## Slide 10: Solution tablets
Compressed tablets to be used for preparing solutions or imparting given characteristics to solutions must be labeled to indicate that they are not to be swallowed.
Examples of these tablet: Potassium Permanganate Tablets for Solution
Effervescent Tablets:
In addition to the drug substance, these contain sodium bicarbonate and an organic acid such as tartaric or citric.
In the presence of water, these additives react liberating carbon dioxide which acts as a distintegrator and produces effervescence.
Except for small quantities of lubricants present, effervescent tablets are soluble.

## Slide 11: Solution tablets
Some newer approaches use tablets that melt at body temperatures. The matrix of the tablet is solidified while the drug is in solution. After melting, the drug is automatically in solution and available for absorption, thus eliminating dissolution as a rate-limiting step in the absorption of poorly soluble compounds.

## Slide 12: Buccal tablets:
These are small, flat, oval tablets.
Buccal tablets
Tablets intended for buccal administration by inserting into the buccal pouch may dissolve or slowly; therefore, they are formulated and compressed with sufficient pressure to give a hard tablet.

## Slide 13: Buccal tablets

## Slide 14: Sublingual tablets
Tablets those containing nitroglycerin, isosorbide dinitrate are placed under the tongue.
Sublingual tablets dissolve rapidly and the drug substances are absorbed readily by this form of administration.

## Slide 15: Molded tablets
Molded tablets(Tablet triturates)
Tablet triturates usually are made from moist material using a triturate mold which gives them the shape of cut sections of a cylinder. Such tablets must be completely and rapidly soluble. The problem arising from compression of these tablets is the failure to find a lubricant that is completely water soluble

## Slide 16: Dispensing Tablets
These tablets provide a convenient quantity of potent drug that can be incorporated readily into powders and liquids, thus circumventing the necessity to weigh small quantities. These tablets are supplied primarily as a convenience for extemporaneous compounding and should never be dispensed as a dosage form.

## Slide 17: Hypodermic Tablets
Hypodermic tablets are soft, readily soluble tablets and originally were used for the preparation of solutions to be injected. Since stable parenteral solutions are now available for most drug substances, there is no justification for the use of hypodermic tablets for injection.
Their use in this manner should be discouraged since the resulting solutions are not sterile. Large quantities of these tablets continue to be made, but for oral administration. No hypodermic tablets ever have been recognized by the official compendia

## Slide 18: Compressed tablets
In order for medicinal substances, with or without diluents, to be made into solid dosage forms with pressure, using available equipment, it is necessary that the material, either in crystalline or powdered form, possess a number of physical characteristics. These characteristics include the ability to flow freely, cohesiveness and lubrication