## Slide 1: SAP-1
Simple As Possible Computers

## Slide 2: 10-1 Architecture

## Slide 3: 10-1 Architecture
PROGRAM COUNTER
Program counter is a part of the control unit of SAP and counts from 0000 to 1111.
The program is stored at the beginning of the memory with the first instruction at binary address 0000, second instruction at 0001 and so on.
Its job is to send to the memory the address of the next instruction to be fetched and excuted.
The PC is reset to 0000 before each computer run.
When computer run begins, PC sends address 0000 to the memory.
The PC is then incremented to get 0001.
After the first instruction is fetched and executed, the PC send address 0001 to memory and PC is incremented to 0010….
In this was program counter is keeping track of the next instruction to be fetched and executed

## Slide 4: 10-1 Architecture
INPUT AND MEMORY ADDRESS REGISTER (MAR)
MAR is a part of SAP-1 memory.
During a computer run, the address in the PC is latched into MAR. A bit later, the MAR applies this 4 bit address to the RAM, where a read operation is performed.
THE RAM
The RAM is a 16 X 8 static TTL RAM.
During a computer run, the RAM receives 4-bit addresses from the MAR and a read operation is performed.
In this way, the instruction or data word stored in the RAM is placed on W-bus for use in other parts of the computer

## Slide 5: 10-1 Architecture
INSTRUCTION REGISTER (IR)
IR is a part of the control unit.
To fetch an instruction from the memory, the computer does a memory read operation.
This places the contents of the addressed memory location on the W bus.
At the same time, the instruction register is set up for loading on the next positive clock edge.
The contents of the IR are split into 2 nibbles. The upper nibble goes to the controller sequencer and the lower nibble is read onto the W-bus when needed.

## Slide 6: 10-1 Architecture
CONTROLLER SEQUENCER
Before each computer run, a CLR’ signal is sent to the PC and a CLR signal is sent to IR. This resets the PC to 0000 and wipes out the last instruction in the IR.
A clock signal CLK is sent to all the buffer registers (MAR, Accumulator, B Register and Output Register)
A CLK’ signal also goes to PC.
The 12 bits that come out of the controller-sequencer form a word controlling the rest of the computer. The 12 wires carrying the control word are called the control bus.
Control word has the format:
CPEPLM’CE’ L1’E1’LA’EA SUEULB’LO’

## Slide 7: 10-1 Architecture
ACCUMULATOR (A)
Accumulator is a buffer register that stores intermediate answers during computer run.
The accumulator has two outputs. One output goes directly to the adder-subtractor. The other output goes to the W-bus when EA is high.

## Slide 8: 10-1 Architecture
THE ADDER-SUBTRACTOR
SAP-1 uses a 2’s complement adder-subtractor. When SU is low, the sum out of the adder-subtractor is
S = A + B
When SU is high, the difference appears
S = A + B’
(Recall that 2’s complement is equivalent to a decimal sign change)
The adder-subtractor is asynchronous (unclocked). This means that the contents can change as soon as the input word changes. However, these contents appear on the W bus only when EU is high.

## Slide 9: 10-1 Architecture
B REGISTER
B Register is another buffer register, used in arithmetic operations.
A low LB’ and CLK loads the word on W bus into B Register. This is fed into the adder-subtractor to be added or subtracted
OUTPUT REGISTER
At the end of a computer run, the accumulator contains the answer. At this point, we need to transfer the answer to the outside world. This is where the output register is used. When EA is high and LO’ is low, the next positive clock edge loads the accumulator word into the output register.
BINARY DISPLAY
Row of 8 LEDs connected to the output register/port

## Slide 10: 10-2 Instruction Set
LDA
LDA stands for “load the accumulator”.
A complete LDA instruction includes the hexadecimal address of the data to be loaded.
LDA 8H means – load the accumulator with the contents of memory location 8H
If, R8 = 1111 0000
The execution of LDA 8H results in A = 1111 0000

## Slide 11: 10-2 Instruction Set
ADD
ADD is another SAP-1 instruction
A complete ADD instruction includes the hexadecimal address of the word to be added.
ADD 9H means – add the contents of the memory location 9H to the accumulator contents. The sum replaces the original contents of the accumulator.
Suppose A = 0000 0010 and R9 = 0000 0011
During execution of ADD 9H, R9 is loaded in B register to get, B = 0000 0011
And almost instantly the adder-subtractor forms the sum of A and B and loads output onto Accumulator A to give A = 0000 0101

## Slide 12: 10-2 Instruction Set
SUB
SUB is another SAP-1 instruction
A complete SUB instruction includes the hexadecimal address of the word to be subtracted.
SUB CH means – subtract the contents of the memory location CH from the accumulator contents. The difference replaces the original contents of the accumulator.
Suppose A = 0000 0111 and RC = 0000 0011
During execution of SUB CH, RC is loaded in B register to get, B = 0000 0011
And almost instantly the adder-subtractor forms the difference of A and B and loads output onto Accumulator A to give A = 0000 0100

## Slide 13: 10-2 Instruction Set
OUT
The instruction OUT tells the SAP-1 computer to transfer accumulator contents to the output port/register.
OUT is complete by itself since the instruction does not involve data in memory
HLT
HLT stands for halt
HLT marks the end of a program
HLT is complete by itself since the instruction does not involve data in memory

## Slide 14: 10-2 Instruction Set
Memory-Reference Instructions
LDA, ADD AND SUB are called memory-reference instructions because they use data stored in memory.
OUT and HLT are not memory-reference instructions
Mnemonics
LDA, ADD ,SUB, OUT and HLT are the instruction set for SAP-1
These are called mnemonics

## Slide 15: 10-3 Programming SAP-1
MNEMONIC | OP CODE
LDA | 0000
ADD | 0001
SUB | 0010
OUT | 1110
HLT | 1111
The Op-code goes to the upper nibble and the operand goes to the lower nibble.
LDA FH = 0000 1111
ADD EH = 0001 1110
HLT = 1111 XXXX
Assembly language involves working with mnemonics when writing a program
Machine language involves working with 0s and 1s